An Event Database for Rotational Seismology
Salvermoser, J., B. Chow, C. Hadziioannou, S. Hable, C.-M. Ramos Domke, J. Wassermann, U. Schreiber, A. Gebauer and H. Igel

Introduction/Motivation:
- Why rotational measurements?
- Summary of related previous studies: Igel et al. (2005 & 2007), Hadziioannou et al. (2012), …
- Intention of the project:
  - make processed data publicly available → browse waveforms and parameters by events
  - present guides and python (open access) source-code examples to download ring laser waveforms → teaching by ipython notebooks!?
  - Provide meta-data (peak-values, SNRs, ...) to public which can be processed by openly

Database:
- Currently running data of one station: Wettzell
  → short station description (not too specific!): G-Ring, Broadband seismometer
  → Aim: include waveforms from PFO, Christchurch, Gran Sasso?, FFB
- Features:
  - GCMT catalog
  - Download example code
  - Search parameters
  - Map
  - Popup-Menue
  - Event availability notes (Which events are available?)

Processing (Using Obspy mainly)
1. Check for new events: (daily automatic updates)
  → Checks GCMT-catalog for new events (Moment magnitude catalog): usually Mw >4.5
2. Download raw Ring laser and broadband seismometer waveforms according to fetched event origin time (from event-xml)
3. Preprocessing split in 3 categories according to epicentral distance:
  Table 1:
	Distance / range	Lowpass / cutoff	Resampling decimation factor	Cross-correlation / window lenght
close	0 <= d <= 3°	4 Hz	2	3 s
local	3° < d <= 10°	2 Hz	2	5 s
tele	d > 10°	1 Hz	4	120 s

1. Remove instrument response of seismometer recordings (velocity) → [nm/s] and adjust sensitivity of ring laser to [nrad/s], deviate acceleration [nm/s²] from seismometer velocity
2. Filter according to table 1
3. Phase velocity and Backazimuth estimation:
  1. Love wave phase velocities:
    1. Rotate seismometer’s accelerations from North-East to Radial-Transverse to match the ring laser rotation rate phase. Use theoretical Baz from source receiver geometry!
    2. Split the signal traces into subwindows (length according to table 1) and for each subwindow apply cross-correlation between vertical rotation rate and transverse acceleration → check the coherence of the two recorded waveforms
    3. For threshold of 75% correlation between the vert. rot. rate and transv. acc. determine phase velocity for the particular time windows that pass this requirement:
      v_ph ` = ` {1}over{2} ` cdot ` { a_t }over{ dot %OMEGA_z }
      using peak values of at and Ωz in the time windows.
    4. Ideally obtain an impression of the dispersive character of Love waves right away, by looking at the temporal evolution of the phase velocity

  - Backazimuth estimation:
    - Analogous to before: split traces into subwindows.
    - For each window estimate the direction of the rotational signal by a grid search optimization algorith:
    - The algorithm checks the correlation between horizontal acceleration and vert. rotation rate by rotating the N-E components in 1°-steps
      → the correlation ismaximum when the rotation angle is equal to best-fitting backazimuth, which is naturally the theoretical Baz
    - For the final estimated BAz value only subwindows that reach 90% max. correlation are considered. The corresponding BAz values is an average over these windows.
    - The conformity of theoretical and estimated BAz is a measure for the conformity of the two recorded measurands (rotation rate, transv. acc.) and thus for the resolution quality of the two instruments.

Conclusions
- Inclusion of other ring lasers (PFO, Christchurch, FFB, Gan Sasso?) in future
- Statistical evaluations:
  - Magnitude scale based on rotational ground motions (Love waves)
  - Local, one-station tomography
  - Analysis of azimuthal effects
- …

References
- Igel et al. (2005): “Rotational motions induced by …”
- Igel et al. (2007): “Broad band observations of earth …”
- Hadziioannou et al. (2012): “Examining ambient noise using co-located …”
- Schreiber et al. (2003): “New applications of very large ring lasers”
- Kurrle et al. (2010): “Can we estimate local Love wave dispersion properties ...”
- Krischer et al. (2015): “Obspy: a bridge for seismology ...”
- Megies et al. (2011): “Obspy – What can it do for data centers ...”
- …

1. Title page with all authors’ names and affiliations, and complete contact information for the corresponding author.
2. Abstracts required for all Regular and Eastern Section articles
3. Text (Introduction, Body, Conclusion)
4. Data & Resources - this section will be required for all SRL articles published in January 2016 and later; requirements are the same as for D&R in BSSA -- see D&R guidelines below.
5. Acknowledgments
6. References
7. Tables
8. Figures for information and fees, see below.
9. Appendixes (optional)
10. Captions for tables and figures
11. Electronic Supplement (optional) - for instructions and fees, see SSA's guidelines for electronic supplements, linked at the bottom of this page.